| Alert Title/ subject: | UNACCEPTABLE DAMAGE TO PSTASS ASSEMBLIES |
| --- | --- |
| ALERT REF NO: | 2016alrt12 – 2/11/2016 |
| REASON FOR ALERT: | Severe damage hAS BEEN caused to PSTASS assemblies Due to incorrect handling both on & offshore. Excessive & unacceptable damage has resultED in pstass (EBS) failure. |
| Description: | Insert Photograph: |
| A recent incident occurred where the non-availability of serviceable PSTASS EBS units offshore led to a passenger having to be removed from a return flight. The EBS units in question after investigation were found to have sustained impact damage that ultimately led to a release of compressed breathing air. The impact damage found is relevant to the PSTASS units being dropped, thrown down or knocked against a hard surface. The photos to the right show the excessive damage seen on a daily basis. Photos 1 & 2 – Photo 3 – Ratchet knob showing signs of impact damage & heavy wear & tear. Label to assist safe operation scraped & torn. |  |
| Description: | Insert Photograph: |
| Photo 4 - Charging port cover dented & part broken off as a result of impact. Photo 5 - Head of PSTASS showing dents & gouges caused by heavy impact. Photo 6 - Internal pin which has bent due to the force of impact. |  |
| Description: | Insert Photograph: |
| Photo 7 - Internal connector showing wear cause by impact against hard surfaces. In addition, heavy impact damage causing internal O-rings to unseat which have led to expulsion of air from the PSTASS cylinder. |  |
| IMMEDIATE RECOMMENDATIONS: |
| Bulletin to be distributed to all heliports & customers/users of the MK50 lifejacket & PSTASS EBS. All passengers, ground and offshore handling personnel to be made aware that failure to handle potentially life-saving survival equipment with adequate care may cause the equipment to fail to function correctly. |
| ACTIONS TO PREVENT RECURRENCE: |
| Equipment damaged by handling or user misuse will be recorded and reported for discussion with the applicable customer and helicopter operator. Proposed improvements to the MK50 lifejacket transportation bag – recommend the use of a padded bag with inner liners attached that can be placed between each lifejacket/PSTASS to provide additional protection during transportation. Survitec will support a revised holdall for review and proposed introduction as standard. Prominent display of this alert at heliports & offshore installations. passengers & handling staff to be made aware of the importance of treating survival equipment with due care & attention Survitec heliport staff to monitor & report all incidents of misuse & associated damage |

Post for 30 days minimum